## Slide 1
Presented By: Felix Ottofuelling
Business Development Manager EU
Intrepid Control Systems, Inc.
Email : fottofuelling@intrepidcs.com
ASAM CMP Protocol Motivation and Overview

## Slide 2: Agenda
What is the ASAM CMP Protocol
Evolution of ASAM CMP Standard
Supported Data Messages: streaming/transmission
System Architecture
Message Overview
Transport over ETHERNET
Cooperation Partners / Interoperability
Configuration 3G Explorer
CMP support in Wireshark
Summary
Next Steps

## Slide 3
What is ASAM CMP
CMP (Capture Module Protocol) – standardised by ASAM
Network Trends:
E/E Networks becoming very large (60 x CAN/LIN + Automotive ETH + FlexRay + ….)
Monolithic Loggers cannot log all the different data
Not sufficient interface counts on one logger (Box is too big)
Solution of CMP:
Decomposition of the logging system (Sink + Interfaces)
Modular architecture
Reuse of interfaces in various applications (in vehicle / HIL
Mix and match different vendors (no vendor login)
Notes: Vehicle EE Networks count became very large in recent years
A single logger cannot cope with the large number of networks in CAN, LIN, FlexRay, and Automotive Ethernet.
Shift of logger design:
Focus on loggers with many Ethernet ports + combining many different interfaces for the local networks to stream data over Ethernet to a data sink
CMP Solution:
Brake logging and network interface apart in 2 separate domains

## Slide 4
What is ASAM CMP
Data Sink
Interfaces
ASAM CMP
Transport options: IEEE 802.3 Ethernet Frame or UDP
Notes: The Probes are synonymous with network interfaces for CAN, LIN AE, FlexRay, etc.
The Interfaces support Ethernet output and stream the data to a data sink – synonumous as data logger
The Probs send CMP Data over IEEEE 802.3 Ethernet or UDP frames to the sinks

## Slide 5
Proprietary Protocols from” technica Engineering”
PLP – Probe Logger Protocol
TECMP – Technical Enhanced Probe Logger Protocol
BMW initiated the ASAM standardization process with a leadership role by technica.
Evolution of ASAM CMP Standard
PLP (… 2014)
TECMP (… 2018)
Data Sink
Capture Module
streaming
ASAM CMP (V1.0.0 / 2022)
Data Sink
Capture Module
streaming & transmission
ASAM CMP (V1.1.0 / 2026)
Notes: With arriving of Automotive Ethernet in the vehicle technica Engineering introduced the PLP Protocol with the first capture modules
Technica coined the term „probe“ as an interface to a network mainly aiming for AE taps
Many Logger Vendors in Europe implemented PLP to capture Data from the technica CM100 and CM1000 high
Then Technica changed it to TECMP, and all Logger Vendors had to implement TECMP
Downside: Logger vendors were always obliged to chase technica’s protocol standards and had development costs and timing delays
To avoid these ongoing changes to and open the market to other capture module vendors, BMW pushed the standardization process over the ASAM Organization
The first release V1.0 was streaming data sink direction only
The Evolution 2026 V1.1. supports for some data formats transmission / downstream commands
The transmission was implemented to operate the interfaces on HIL systems

## Slide 6: CMP Supported Data Messages
Data Message Type | Captured Data | Transmit Data
CAN | V1.0.0 | V1.1.0
CAN FD | V1.0.0 | V1.1.0
LIN | V1.0.0 | V1.1.0
FlexRay | V1.0.0 | V1.1.0
Digital | V1.0.0 | 
UART RS232 | V1.0.0 | 
ANALOG | V1.0.0 | 
ETHERNET | V1.0.0 | V1.1.0
Data Message Type | Captured Data | Transmit Data
SPI | V1.0.0 | 
I2C | V1.0.0 | 
GigE Vision | V1.0.0 | 
MIPI | V1.0.0 | V1.1.0
RAW ETHERNET | V1.0.0 | V1.1.0
10BASE-T1S | V1.0.0 | 
A2B* | V1.0.0 | 
Vendor specific | V1.0.0 | 
* Aligned to RAD A2B
Notes: In the latest release V1.1 3 new data formats where introduces
Ethernet RAW
10BASE-T1S
A2B > Was in particular pushed by Andreas and Felix from the German office.
Thanks to the help and development team in UK Fabio and Mike Warner and US team Bryant Jones.

## Slide 7
Work Group Contributors
AUDI AG
b-plus GmbH
BMW AG
dSPACE GmbH
ETAS GmbH
Intrepid Control Systems GmbH
Technica Engineering GmbH
Vector Informatik GmbH
VIGEM GmbH
CMP Work Group & Supporters
ASAM CMP Adopters / Implementation
IPETRONIK
AKKODIS
Tracetronik
Dewesoft X
openDAQ API
RAC Consulting
X2E
G.I.N
WIRESHARK (Plugin by Lars Völker)
Notes: Here we see a list of companies actively contributing to the creation and evolution of the ASAM CMP standard.
The other companies have ASAM CMP implemented.
We can see that CMP is widely implemented provides a huge benefit for technica and the logger vendors
Every party has a referencen for implementation and plug and play is more easy to achieve

## Slide 8: System Architecture
System Implementation Scope
Multiple Capture Modules
Multiple Streams
Multiple Data Sinks
Tims synchronization
gPTP + new PTPv2
Notes: The system architecture highlights 3 main functionalities:
The system can work with multiple capture modules / interfaces
The capture modules can support multiple data formats e.g. CAN, FlexRay, LIN in dedicated “streams”
AND on top the architecture supports the streaming to multiple data sinks.
We have seen OEM having 3 different logging systems in the vehicle trunk logging the data for different teams with tansfer to different data lakes

## Slide 9: CMP Messages Components
Notes: The CMP Message is composed of different messages - all organized in a HEADER and PAYLOAD structure.
Data Message: Payload for the different data formats CAN, LIN, I2C, A2B…. Reflecting a specialities of the data format “FlexRay” Cycles, A2B Super frames, 10BASET1S Symbols
Status Message: Cyclic and event-based status messages
>providing information about the capture module time sync, #SN, HW+SW revision …. Vendor Infos
> Status of the interface: up, down, disables, type of network,
Control Messages: About communication with the data sink - ready for transmission or receiving, wait, pause, interface counter
Vendor defined message – sandbox for special functions

## Slide 10: CMP Transport via ETHERNET/UDP Mesg.
Destination MAC can be defined in 3G Explorer
Notes: CMP Message are transfer either ovder Ethernet Frame or UDP
ICS did the Ethernt Frame implementation

## Slide 11
RED2
RAD Gigastar
FIRE 3
Interfaces
Modular / Expandable
(RAD A2B)
Cooperation ICS x Data Sink Vendors
Tested / Implemented
Future
RAD Galaxy2
RAD Gigastar 2
RAD COMET2/3
Cooperation & tests
No-Cooperation
ASAM CMP
CAN, LIN, Ethernet
Automotive Ethernet, A2B
G.I.N.
ViGEM
Dewesoft X
b-plus
Logger /
Data Sink
IPETRONIK
AKKODiS
Notes: Here we can see that ICS is already cooperating and working with different data sink manufacturers together to test CMP communication.
All partners had a RED2 demo interface and tested at least the CAN communication of ASAM CMP
GIN rejected any cooperation so far– hoever they are required to work with VW on fleetlogging with RAD A2B

## Slide 12
CMP in 3G Explorer
Example screenshot from
RAD A2B interface
Interface IDs are defined in 3G explorer: /CAN IDs - 0x01- 0xFF/ /LIN IDs - 0x0101- 0x01FF/ /FleyRay IDs - 0x0201- 0x02FF/ /Ethernet IDs - 0x0301- 0x03FF/ /DIO IDs - 0x0401- 0x04FF/ /Serial IDs - 0x0501- 0x05FF/ /SPI IDs - 0x0601- 0x06FF/ /DIO IDs - 0x0701- 0x07FF/
* Activate coremini for CMP output
Notes: Here we see the 3G configuration interface for CMP
One workflow obstacle is that coremini must be activated with VSpy to make CMP output work.
Logger customers have the 3G explorer but not necessarily a vSpy license
It would be good if we could overcome this additional config requirement somehow?

## Slide 13
ASAM CMP Data in Wireshark*
The Stream Instance ( 1…3) is not presented in Wireshark! – optional setting to send data to up to 3 loggers at the same time.
* Activate CMP Data Display – see next page.
Device ID
Stream ID
Interface ID

## Slide 14
Activate CMP in Wireshark
Notes: In the decoding options in Wireshark, you can activate the ASAM CMP decoding.

## Slide 15
PoC Project – CLAAS x IPETRONIK
RAD Galaxy + IPETRONIK Data Logger
Slave
ECU 1
2x 100BASE-T1
Tap Mode
ASAM CMP
LAN 1000BASE-T
ETH2 / ETH3
Logger IPE853

## Slide 16
CMP Activation in IPEmotion RT
192.168.2. „Device ID“
Stream ID

## Slide 17
CMP Data in IPEmotion RT

## Slide 18: Summary of ASAM CMP
ASAM CMP is widely adopted by logger suppliers in Europe
Besides Technica and ICS no other capture module suppliers is identified so far
ASAM CMP supports interface sales in combination with established logger suppliers
Opens door to replace technica boxes CM1000 HIGH, CAN Combo, LIN Combo,
Marketing is important
ASAM CMP should be integrated to VSPY 3 HW manual
Integration to ICS Website

## Slide 19: Next Steps
Integration test across all data formats to be done (CAN, LIN, Automotive Ethernet)
PoC with Claas
PoC with Volvo Trucks x IPETRONIK ARCOS Logger (replacing CAN & LIN Combo)
PoC with VW for RAD A2B x ViGEM Logger (GIN)
Developments:
Propose CMP Implementation for 10BASE-T1S Tools (need for Scania)
Propose CMP transmission function (new V1.1.0) for CAN, LIN
Simplify the coremini activation requirement
ICS becomes a data sink – when new logger can stream > 1 Gigabit/s

## Slide 20: Thank you!
If you have any questions or require any additional information, please don’t hesitate to ask.
Felix Otofuelling
Business Development Manager EU
fottofuelling@intrepidcs.com